#### PREFLIGHT CHECKLIST – N931SJ (C182S)

CABIN

- Documents (AROW)	ON BOARD

- Squawks/Tach/Fuel/Oil/VOR/Inspections	VERIFY

- Control Lock, Covers, Tie-Downs	REMOVE

- Electric Pre-Heater Cable	UNPLUG & STOW

- Master & Ignition	VERIFY OFF

- Avionics & Electrical Switches	OFF

- Master Switch	ON

- Fuel Gauges & Annunciators	CHECK

- Avionics Master	ON (hear fan, then OFF)

- Static Pressure Alternate Source Valve	OFF

- Annunciator Panel Switch	TEST / MESSAGES?

- Clock	VERIFY = LOCAL TIME

- Flaps	EXTEND

- Pitot Heat (IFR)	ON (warm <30 sec, then OFF)

- Lights & Stall Warning	CHECK

- Master Switch	OFF

- Seat Stops & Fire Extinguisher	CHECK

- Manifold Pressure	VERIFY = LOCAL ALTIMETER

- Baggage Door	SECURE

#### PREFLIGHT CHECKLIST – N931SJ (C182S)

EXTERIOR

- Fuel Sumps	CHECK (5 each wing, 2 belly)

- Fuel Quantity, L & R Tanks	OPEN & VERIFY

- Fuel Filler Caps	CHECK VENTS

- Oil Level	VERIFY 6+ quarts

- Left Side Fuselage	CHECK

- Empennage	CHECK

- Trim Tab	CHECK SECURITY

- Right Side Fuselage	CHECK

- Right Flap, Aileron, Wing & Wingtip	CHECK

- Right Tire & Brake	CHECK

- Static Port (right side)	CHECK CLEAR

- Cowl, Prop & Spinner	CHECK

- Air Intake	CHECK CLEAR

- Nose Wheel & Strut	CHECK

- Pitot Tube & Fuel Vent	CHECK

- Left Wing & Wingtip, Flap, Aileron	CHECK

- Left Tire & Brake	CHECK

- Static Port (left side)	CHECK CLEAR

- Wheel Chocks	REMOVE

# Watch wingtips & tail when pulling out of the hangar!

# Remember: 1SJ has a landing weight limitation of 2950 lbs.

ENGINE START CHECKLIST – N931SJ (C182S)

- Seats & Belts	SET & SECURED

- Passenger Briefing	COMPLETE

- Circuit Breakers	IN

- Beacon (+Nav for night ops)	ON

- Avionics Master & Electrical	OFF

- Cowl Flaps	OPEN

- Fuel Selector Valve	OFF, then BOTH

- Throttle	OPEN ¼”

- Propeller	HIGH RPM

- Mixture	IDLE CUTOFF

- Prop Area	VISUALLY CHECK CLEAR

- Brakes	APPLY & HOLD

- Master Switch	ON

- Auxiliary Fuel Pump Switch	ON

- Mixture	ADVANCE (see rise, then IDLE CUTOFF)
* Skip this step (priming) if engine is already warm.

- Auxiliary Fuel Pump Switch	OFF

- Ignition	START

- Mixture	ADVANCE to FULL RICH as engine starts
If engine floods:

- Fuel Pump OFF, Mixture IDLE CUTOFF

- Throttle	OPEN ½ TO FULL

- Ignition	START

- Mixture	FULL RICH (as engine starts)

- Throttle	RETARD once engine starts

- Oil Pressure	IN THE GREEN (within 30 sec.)

- Throttle	1000 RPM

- Mixture	LEAN FOR TAXI

- Flaps	RETRACT

- Avionics Master Switch & Radios	ON

- Autopilot	CHECK OFF (beep)

- Listen to AWOS	GET WX, WIND, ALT, RUNWAY

- Transponder	SET / ALT

- Altimeter	SET (and set value in autopilot BARO)

- GPS	CHECK RAIM

- Heading Indicator	SET TO MAG COMPASS

# NORMAL CHECKLIST – N931SJ (C182S)

# TAXI

- Taxiway	VISUALLY CHECK CLEAR

- Brakes	TEST BOTH SIDES

- Airspeed Indicator, VSI	CHECK FOR “0”

- Left Turns	CHECK
* Wing left, ball right, DG -, MC -

- Right Turns	CHECK
* Wing right, ball left, DG +, MC +

- Attitude Indicator	< 5 DEG IN TURN

- Magnetic Compass	NO CRACKS, NO BUBBLES

- Altimeter	FIELD ELEV +/- 75 feet

- Alternate Static	TEST

- Vacuum, Alternator, Amp	IN THE GREEN

# NORMAL CHECKLIST – N931SJ (C182S)

# ENGINE RUNUP – SYSTEMS CHECK

- Nose Wheel	STRAIGHT

- Brakes	SET

- Flight Controls	FREE & CORRECT

- Fuel Selector & Quantity	CHECK

- Autopilot
Electric Trim	NOSE DOWN/UP
* Verify trim wheel stops moving when AP disconnect 
button is pressed. 
Autopilot	ENGAGE (press AP button)
Flight Controls	VERIFY overpower (PITCH/ROLL)
A/P DISC	PRESS (hear beep, verify OFF)

- Elevator & Rudder Trim	SET FOR TAKEOFF

- Heading Indicator	SET TO MAG COMPASS

- Radio, Nav/GPS & Transponder	SET

- Mixture	ADVANCE ½ WAY TO RICH

- Throttle	1800 RPM
* Check for all engine & suction gauges in green.

- Ammeter	CHECK

- Magnetos (L then R)	CHECK
* Max 150 rpm drop each, <50 differential L/R.

- Propeller	CYCLE
* Check for drops in oil pressure & manifold pressure.

- Suction	CHECK (4.5-5.5” Hg)

- Annunciator Panel	CHECK, NO MESSAGES

- Throttle	800-1000 RPM

- Brakes	RELEASE

# NORMAL CHECKLIST – N931SJ (C182S)

BEFORE TAKEOFF

- Passenger Briefing	COMPLETE
* Sterile cockpit; how to exit in an emergency.

- Pilot Self-Briefing	COMPLETE
* Departure plan? Emergency?

- Autopilot	OFF

- Flaps	0-20 Degrees

- Trim	SET FOR TAKEOFF

- Mixture	FULL RICH

- Doors, Windows, Seats & Belts	SECURE

- Transponder	SET & ALT

- Strobes & Landing Lights	ON

- Pitot Heat	AS REQUIRED

- Final Approach	CHECK FOR TRAFFIC

- Taxi Onto Runway	ANNOUNCE

- Heading Indicator	SET TO COMPASS / RUNWAY

Takeoff Static RPM 2350-2400

Rotate 55, Climb 70-80, Flaps Up, “Top of Greens”

SHORT FIELD TAKEOFF

- Flaps	20 Degrees

- Brakes	APPLY

- Power	FULL THROTTLE and 2400 RPM

- Brakes	RELEASE

- Elevator Control	MAINTAIN SLIGHTLY TAIL-LOW

- Climb	58 Knots until clear of obstacles

- Flaps 	RETRACT slowly after 70 Knots

# NORMAL CHECKLIST – N931SJ (C182S)

Normal Climb	85-95 Knots

Maximum Performance Climb	70-80 Knots

Vx = 63

Vy = 80

# CRUISE

- Power	15-23”, 2100-2400 RPM*

- Elevator and Rudder Trim	ADJUST

- Mixture	LEAN

- Cowl Flaps	CLOSED

- Unnecessary Lights (eg. Landing)	OFF

- Engine/Flight Instruments	CHECK OFTEN !!

# * Refer to Skylane Configurations table.

# BEFORE LANDING

- Get Weather, Runway Info	LISTEN TO AWOS

- Altimeter	SET

- Heading Indicator	SET TO MAG COMPASS

- Fuel Selector Valve	BOTH

- Mixture, Prop	FULL FORWARD

- Seatbelts	SECURE

- Landing Light, Runway Lights	ON

GUMPAC

Gas, Undercarriage, Mixture, Prop, Autopilot OFF, Carb Heat ON

# Final Approach:

# 60-70 knots flaps DOWN

70-80 knots flaps UP

# NORMAL CHECKLIST – N931SJ (C182S)

# AFTER LANDING

- Hold Short Line	TAXI TO CLEAR

- Flaps	RETRACT

- Cowl Flaps	OPEN

- Strobes & Landing Light	OFF

- Mixture	LEAN

- IFR Flight Plan	CANCEL IF REQUIRED

# AIRCRAFT SHUTDOWN

- ELT 121.5	MONITOR

- Avionics Master, Lights	OFF

- Throttle	IDLE

- Magneto Grounding	CHECK

- Throttle	1500 RPM

- Fuel Selector	RIGHT TANK

- Mixture	IDLE CUTOFF

- Ignition, Master Switch	OFF & REMOVE KEY
* Use caution pushing plane back into hangar!

- Control Lock, Tie Downs, Sun Covers	INSTALL

- Squawks/Tach/Fuel/Oil/VOR	RECORD

- Doors	LOCK

- Electric Pre-Heater	PLUG IN

Call for fuel if required. Fill TO THE TABS ONLY.
Close flight plan. Take your trash with you! (

EMERGENCY CHECKLIST – N931SJ (C182S)

ABORTED TAKEOFF

- Throttle	IDLE

- Brakes	APPLY

- Wing Flaps	RETRACT

- Mixture	IDLE CUTOFF

- Ignition, Master Switch	OFF

###### ENGINE FAILURE AFTER TAKEOFF

- Airspeed	75 (70 Flaps Down)

- Mixture	IDLE CUTOFF

- Fuel Selector Valve	OFF

- Flaps	FULL

- Ignition, Master Switch	OFF

- Doors	UNLATCH

###### ENGINE FAILURE IN CRUISE

- Airspeed	75 (Best Glide)
Look for a suitable landing field: land into wind if possible. Attempt a restart:

- Fuel Selector Valve	BOTH

- Auxiliary Fuel Pump	ON

- Mixture	FULL RICH

- Ignition	BOTH (test L & R mags)

If engine does not restart:

- “MAYDAY – ENGINE OUT”	Unicom, 121.5

- Airspeed	75 (70 Flaps Down)

- Mixture	IDLE CUTOFF

- Fuel Selector Valve	OFF

- Ignition Switch	OFF

- Flaps	FULL

- Master Switch	OFF  (when landing is assured)

- Doors	UNLATCH BEFORE TOUCHDOWN

###### EMERGENCY CHECKLIST – N931SJ (C182S)

###### FIRE DURING ENGINE START

- Cranking	CONTINUE

- Power	1700 (for a few minutes), then shut down

If engine does NOT start, continue cranking:

- Throttle	FULL OPEN

- Mixture	IDLE CUTOFF

- Fuel Selector Valve	OFF

- Auxiliary Fuel Pump	OFF

- Fire Extinguisher	GRAB (between front seats)

- Ignition, Master Switch	OFF

- Fire Extinguisher	SPRAY AT BASE OF FIRE

###### FIRE IN FLIGHT

- Mixture	IDLE CUTOFF

- Fuel Selector Valve	OFF

- Auxiliary Fuel Pump, Master Switch	OFF

- Cabin Heat & Vents	CLOSED

- Airspeed	100 Knots +++

###### AUTOPILOT FAILURE

- Control Wheel	GRASP FIRMLY

- A/P DISC / TRIM INT Switch	PRESS & HOLD

- Manual Trim	RE-TRIM AS NECESSARY

- A/P CIRCUIT BREAKER	PULL (or MASTER OFF)

Use above sequence in response to any of the following messages:

PITCH TRIM = electric trim malfunction, even with A/P OFF.

P = pitch axis disabled	R = roll axis disabled

HDG = failed heading	GS = flagged glide slope

NAV, ARP, REV = flagged navigation source